Pseudo Code for Lazy Larry

Kyla Barr, Abigail Soong, and Kathy Spriggs

______________________________________________________________________

We will use the ME218 Event Framework written by Ed Carryer.

This code uses a single state machine called: LarryActions

Assumed Connections:

| Startup Sensor | T5 |
| --- | --- |
| Pick Up Sensor | AD0 |
| Poke Sensor | M2 |
| Eyes Covered Sensor | AD1 |
| Eyes Motor | T2 |
| Right Arm Motor | T3 |
| Left Arm Motor | T4 |
| Ear Motors | T0 & T1 |
| Buzzer | M4 |

______________________________________________________________________

Main Module

This .c file contains the main function.

_____________________________________________________________________

Main Function

/**************************************************************************** Function Main()

Runs an infinite loop checking for events and then responding to events.

Parameters: None

Returns: None

Author J. Edward Carryer, 10/23/11

****************************************************************************/

Initialize microcontroller

Set I/O on data register

Set initial values

Initialize Timers

Initialize Servos

Initialize PWMS12

Initialize the event framework (EF_Initialize)

Initialize state machines

Start state machines

Initialize variable ErrorType as equal to EF_Initialize()

if ErrorType is successful

ErrorType is equal to EF_Run();

If an error breaks the EF_Run() loop above:

Based on the value of ErrorType choose one of the following blocks of code:

if ErrorType is FailedPointer

print “Failed on NULL pointer

if ErrorType is FailedInit

print “Failed Initialization:

else

print “Other Failure”

end switch statement

“for (;;);”

end Main function

____________________________________________________________________________

Init Module

This .c file contains the init functions for all hardware.

The .h file prototypes for PortC32Init() and InitServos() called in the main function

_____________________________________________________________________

PortC32Iinit() Function

/**************************************************************************** Function PortC32Init()

Initializes ports of C32.  Such that:

T0 Output

T1 Output

T2 Output

T3 Output

T4 Output

T5 Input

M2 Input

M4 Input

AD0 Analog Input

AD1 Analog Input

Parameters: None

Returns: None

Author J. Edward Carryer, 10/23/11

****************************************************************************/

Set DDRT to 0x1F

Set DDRM to 0x10

Set AD0, AD1 to analog inputs.

End PortC32Init function.

InitServo() Function

/**************************************************************************** Function InitServos()

Uses servo module to set ports T0-T4 as servo outputs.  Sets initial positions of servo motors.

Parameters: None

Returns: None

Author J. Edward Carryer, 10/23/11

****************************************************************************/

If servo initialization of T0-T4 is successful

if RightArmDown() && LeftArmDown() && EarsWiggleIn() are successful

print “We are starting in the right place”

print “Servos are Initialized”

End of InitSensors funciton.

______________________________________________________________________

EventCheckers Module

This .c file contains the EventChecker functions.

The .h file includes prototypes for:

CheckStartupEvents()

CheckPokeEvents()

CheckEyesCoveredEvents()

CheckPickUpEvents()

CheckEyesClosingTimer()

CheckGameTime ()

CheckActionTimer ()

CheckBeepTimer()

CheckEarTimer ()

CheckInterimTimer()

CheckActionSequenceEvents ()

ResetGameTimer ()

Data private to the module:

Defined variables:

//EyesStillCoveredTime (Time to wait before checking if eyes are still covered)

StartDebounceTime

PokeDebounceTime

GAME_LENGTH

EYES_TICKING_TIME

Static variables:

LastStartupState

LastPokeState

LastPickUpState

CurrentPickUPInt

IRLEDDebounce

LastTime

GameTime

_____________________________________________________________________

CheckStartupEvents() Function

/**************************************************************************** Function CheckStartupEvents()

Checks for start button pressed to start the game.

Parameters: None

Returns: boolean TRUE if an event was detected, FALSE otherwise

Author Katherine Spriggs, 11/17/11

****************************************************************************/

local variable ReturnVal is FALSE

local variable CurrentStartupState

If start debounce time has expired

read CurrentStartupState from pin T5

If CurrentStartupState is not the same as LastStartupState

If CurrentStartupState is hi

PostEvent EF_StartPressed

Start start debounce timer

ReturnVal is TRUE

Else (CurrentStartupState is lo)

Do nothing

Set LastStartUpState to CurrentStartupState

Return ReturnVal

End CheckStartupEvents function

CheckPokeEvents() Function

/**************************************************************************** Function CheckPokeEvents()

Checks for poke events.

Parameters: None

Returns: boolean TRUE if an event was detected, FALSE otherwise

Author Katherine Spriggs, 11/17/11

****************************************************************************/

local variable ReturnVal is FALSE

local CurrentPokeState

If poke debounce time has expired

read CurrentPokeState from pin M2

If CurrentPokeState is not the same as LastPokeState

If CurrentPokeState is hi

PostEvent EF_Poke

start poke debounce timer

ReturnVal is TRUE

Else (CurrentPokeState is lo)

Do nothing

LastPokeState = CurrentPokeState

Return ReturnVal

end CheckPokeEvents function

CheckEyesCoveredEvents() Function

/**************************************************************************** Function CheckEyesCoveredEvents()

Checks for eyes covered events.

Parameters: None

Returns: boolean TRUE if an event was detected, FALSE otherwise

Author Katherine Spriggs, 11/17/11

****************************************************************************/

local variable ReturnVal is FALSE

local CurrentEyesCoveredState

if eyes covered debounce timer has expired

read CurrentEyesCoveredState from pin AD0

If CurrentEyesCoveredState is greater than 500 and not equal to 1023

PostEvent EF_EyesCovered

start eyes covered debounce timer

ReturnVal is TRUE

Return ReturnVal

end CheckEyesCoveredEvents function

CheckPickUpEvents() Function

/**************************************************************************** Function CheckPickUpEvents()

Checks for changes in pick up height.

Parameters: None

Returns: boolean TRUE if an event was detected, FALSE otherwise

Author Katherine Spriggs, 11/17/11

****************************************************************************/

local variable ReturnVal is FALSE

local CurrentPickUpState

Read CurrentPickUpState from pin AD1

Choose one of the following blocks of code based on LastPickUpInt

(These lines implement hysterisis for analog readings of pick up height)

if LastPickUpInt is 0

if 250 <= CurrentPickUpState <= 300

CurrentPickUpInt = 1

else

CurrentPickUpInt = 0

if LastPickUpInt is 1

if 100 < CurrentPickUpState <= 250

CurrentPickUpInt = 2

else if CurrentPickUpState >= 500

CurrentPickUpInt = 0

else

CurrentPickUpInt = 1

if LastPickUpInt is 2

if CurrentPickUpState <= 50

CurrentPickUpInt = 3

if 350 <= CurrentPickUpState <= 500

CurrentPickUpInt = 0

else

CurrentPickUpInt = 2

if LastPickUpInt is 3

if 250 <= CurrentPickUpState <= 300

CurrentPickUpInt = 2

else

CurrentPickUpInt = 3

end switch statement

if CurrentPickUpInt is not equal to LastPickUpInt

if CurrentPickUpInt is not equal to 0

post event EF_PickedUp

send event parameter CurrentPickedUpInt

ReturnVal is TRUE

else

post event EF_PutDown

ReturnVal is TRUE

LastPickUpInt = CurrentPickUpInt

return ReturnVAl

end CheckPickUpEvents function

CheckGameTime() Function

/**************************************************************************** Function CheckGameTime()

Checks if the game timer has expired.

Parameters: None

Returns: boolean TRUE if an event was detected, FALSE otherwise

Author Katherine Spriggs, 11/17/11

****************************************************************************/

local variable ReturnVal is FALSE

local CurrentTime is current global time

if CurrentTime - GameTime >= GAME_LENGTH

if IsGameActive() is TRUE

post event EF_GameTimerExpired

ReturnVal is TRUE

Return ReturnVal

end CheckGameTime function

CheckActionTimer() Function

/**************************************************************************** Function CheckActionTimer()

Checks if the action timer has expired.

Parameters: None

Returns: boolean TRUE if an event was detected, FALSE otherwise

Author Katherine Spriggs, 11/17/11

****************************************************************************/

local variable ReturnVal is FALSE

if IsActionActive() is TRUE

if action timer has expired

post event EF_ActionTimerExpired

ReturnVal is TRUE

Return ReturnVal

end CheckActionTimer function

CheckEarTimer() Function

/**************************************************************************** Function CheckEarTimer()

Checks if the ear timer has expired.

Parameters: None

Returns: boolean TRUE if an event was detected, FALSE otherwise

Author Katherine Spriggs, 11/17/11

****************************************************************************/

local variable ReturnVal is FALSE

if EarsAreOut() is TRUE

if ear timer has expired

post event EF_Ear_Timer_Expired

ReturnVal is TRUE

Return ReturnVal

end CheckEarTimer function

CheckEyesClosingTimer() Function

/**************************************************************************** Function CheckEyesClosingTimer()

Checks if the eyes closing timer has expired.

Parameters: None

Returns: boolean TRUE if an event was detected, FALSE otherwise

Author Katherine Spriggs, 11/17/11

****************************************************************************/

local variable ReturnVal is FALSE

local CurrentTime is current global time

if (CurrentTime - LastTime >= EYES_TICKING_TIME

post event EF_Eyes_Timer_Expired

ReturnVal is TRUE

LastTime is equal to CurrentTime

Return ReturnVal

end CheckEyesClosingTimer function

CheckBeepTimer() Function

/**************************************************************************** Function CheckBeepTimer()

Checks if the beep timer has expired.

Parameters: None

Returns: boolean TRUE if an event was detected, FALSE otherwise

Author Katherine Spriggs, 11/30/11

****************************************************************************/

local variable ReturnVal is FALSE

if IsBeepActive() is TRUE

if beep timer has expired

post event EF_BeepTimerExpired

ReturnVal is TRUE

Return ReturnVal

CheckInterimTimer() Function

/**************************************************************************** Function CheckInterimTimer()

Checks if the interim timer has expired.

Parameters: None

Returns: boolean TRUE if an event was detected, FALSE otherwise

Author Katherine Spriggs, 11/30/11

****************************************************************************/

local variable ReturnVal is FALSE

if IsInterimActive() is TRUE

if interim timer has expired

post event EF_InterimTimerExpired

ReturnVal is TRUE

Return ReturnVal

end CheckInterimTimer function

CheckActionSequenceTimer() Function

/**************************************************************************** Function CheckActionSequenceTimer()

Checks if the interim timer has expired.

Parameters: None

Returns: boolean TRUE if an event was detected, FALSE otherwise

Author Katherine Spriggs, 11/30/11

****************************************************************************/

local variable ReturnVal is FALSE

if IsActionSequenceActive() is TRUE

if interim timer has expired

post event EF_ActionSequenceTimerExpired

ReturnVal is TRUE

Return ReturnVal

end CheckActionSequenceTimer function

ResetGameTimer() Function

/**************************************************************************** Function ResetGameTimer()

Resets the game timer.

Parameters: None

Returns: boolean TRUE if an event was detected, FALSE otherwise

Author Katherine Spriggs, 11/30/11

****************************************************************************/

GameTimer = current global time

end ResetGameTimer function

______________________________________________________________________

LazyLarrySM Module

This .c file contains the LazyLarry State Machine functions.

The .h file includes:

State Definitions:

InitPState

WaitingForStart

WaitingForPoke

WaitingForEyesCovered

WaitingForPickUp

WaitingForPutDown

WaitingBetweenActions

Function Prototypes for:

InitLazyLarrySM()

PostLazyLarrySM()

IsLazyLarrySMQEmpty()

RunLazyLarrySM()

QueryLazyLarrySM()

TurnBuzzerOn()

TurnBuzzerOff()

IsGameActive()

IsActionActive()

IsBeepActive()

EarsAreOut()

IsInterimActive()

IsActionSequenceActive()

getGlobalTime()

RightArmDown()

LeftArmDown()

EarsWiggleIn()

Module Defines:

SERVO_RA 3

SERVO_LA 4

SERVO_LE 1

SERVO_RE 0

SERVO_EYES 2

QUEUE_SIZE 3

BEEP_TIME 100

NOISE_SPACE_TIME 100

EAR_TIME 500

ACTION_TIME 20000

INTERIM_TIME 1000

EYES_CLOSED_TIME 1000

ACTION_SEQUENCE_TIME  500

Static variables:

static LazyLarryState_t CurrentState;

static LazyLarryState_t NextState;

static LazyLarryState_t LastState;

static boolean BuzzerOn;

static boolean GameActiveFlag;

static boolean ActionActiveFlag;

static int BeepCount;

static boolean BeepActive;

static boolean InterimActive;

static boolean EarsOut;

static int CurrentEyesPosition;

static boolean ActionSequenceActive;

static boolean HappyEndSequence = FALSE;

static boolean SadEndSequence = FALSE;

static boolean RerequestPickUp = FALSE;

static boolean RerequestPutDown = FALSE;

static boolean PutDown = FALSE;

static int score = 100;

static EF_Event LazyLarrySMQueue[QUEUE_SIZE+1];

Private Functions:

void RandomlyPickNextState (void);

void RequestAction (void);

void RerequestAction (void);

void DoRerequestPickUpAction(void);

void DoRerequestPutDownAction(void);

void DoPutDownAction(void);

boolean EarsWiggleOut(void);

boolean LeftArmUp(void);

boolean RightArmUp(void);

void LowerArmsHalfWay (void);

void PutArmsDown (void);

void PutArmsUp (void);

boolean OpenEyes(void);

boolean EyesPosition(void);

boolean CloseEyes (void);

void MakeHappyNoise(void);

void DoHappyEndSequence (void);

void DoSadEndSequence (void);

void DoHappyEndSequenceAction (void);

void DoSadEndSequenceAction(void);

void Beep (void);

_____________________________________________________________________

RunLazyLarrySM() Function

/**************************************************************************** Function RunSM()

Checks for start button pressed to start the game.

Parameters: None

Returns: boolean FALSE if error in initialization TRUE otherwise

Author Katherine Spriggs, 11/29/11

****************************************************************************/

For several events, the same code appears in each state of the state machine after the InitPState.  To make the state machine easier to read, the code for each of those events is described here:

if ThisEvent is EF_BeepTimerExpired

if BuzzerOn is TRUE

TurnBuzzerOff()

BuzzerOn is FALSE

Restart beep timer for BEEP_TIME

else if BeepCount is not equal to 0

Beep()

BeepCount is BeepCount -1

else

BeepActive is FALSE

if ThisEvent is EF_EarTimerExpired

EarsWiggleIn()

if ThisEvent is EF_ActionTimerExpired

if HappyEndSequence == TRUE

DoHappyEndSequenceAction()

if SadEndSequence == TRUE

DoSadEndSequenceAction()

if RerequestPickUp == TRUE

DoRequestPickUpAction()

if RerequestPutDown == TRUE

DoRequestPutDownAction()

if ThisEvent is EF_GameTimerExpired

ActionActiveFlag is FALSE

GameActiveFlag is FALSE

if score >105

DoHappyEndSequence()

else

DoSadEndSequence

CurrentState = WaitingForStart

if ThisEvent is EF_ActionTimerExpired

ActionActiveFlag is FALSE

GameActiveFlag is FALSE

DoSadEndSequence()

CurrentState is WaitingForStart

if ThisEvent is EF_Eyes_Timer_Expired

Increment the eyes closing timer (call EyesPosition())

local variable ThisEvent

pull an event from the queue

if ThisEvent equals EF_NO_EVENT

return FALSE

else

choose one of the following blocks of code based on CurrentState

if CurrentState is InitPState

Set CurrentState to WaitingForStart

ActionActiveFlag is FALSE

TurnBuzzerOff()

if CurrentState is WaitingForStart

LastState is WaitingForStart

Choose one of the following blocks of code based on ThisEvent

if ThisEvent is EF_StartPressed

GameActiveFlag is TRUE

InterimActive is FALSE

ResetGameTimer()

Score is 100

OpenEyes()

CurrentEyesPosition is 0

RandomlyPickNextState()

RequestAction

ActionActiveFlag is TRUE

Set action timer

CurrentState is NextState

if ThisEvent is EF_BeepTimerExpired

See event notes at top of function

if ThisEvent is EF_EarTimerExpired

See event notes at top of function

if ThisEvent is EF_ActionTimerExpired

See event notes at top of function

end switch statement

if CurrentState is WaitingForPoke

LastState is WaitingForPoke

Choose one of the following blocks of code based on ThisEvent

if ThisEvent is EF_Poke

MakeHappyNoise()

Add 1 to score

CurrentState is WaitingBetweenActions

InterimActive is TRUE

Start Interim timer for INTERIM_TIME

if ThisEvent is EF_EyesCovered

RerequestAction()

subtract 1 from score

if ThisEvent is EF_PickedUp

RerequestAction()

subtract 1 from score

if ThisEvent is EF_GameTimerExpired

See event notes at top of function

if ThisEvent is EF_ActionTimerExpired

See event notes at top of function

if ThisEvent is EF_Eyes_Timer_Expired

See event notes at top of function

if ThisEvent is EF_Ear_Timer_Expired

See event notes at top of function

if ThisEvent is EF_BeepTimerExpired

See event notes at top of function

if ThisEvent is EF_ActionSequenceTimerExpired

See event notes at top of function

end switch statement

if CurrentState is WaitingForEyesCovered

LastState is WaitingForEyesCovered

Choose one of the following blocks of code based on ThisEvent

if ThisEvent is EF_Poke

RerequestAction()

subtract 1 from score

if ThisEvent is EF_EyesCovered

MakeHappyNoise()

CurrentState is WaitingBetweenActions

InterimActive is TRUE

Start Interim timer for INTERIM_TIME

add 1 to score

if ThisEvent is EF_PickedUp

RerequestAction()

subtract 1 from score

if ThisEvent is EF_GameTimerExpired

See event notes at top of function

if ThisEvent is EF_ActionTimerExpired

See event notes at top of function

if ThisEvent is EF_Eyes_Timer_Expired

See event notes at top of function

if ThisEvent is EF_Ear_Timer_Expired

See event notes at top of function

if ThisEvent is EF_BeepTimerExpired

See event notes at top of function

if ThisEvent is EF_ActionSequenceTimerExpired

See event notes at top of function

end switch statement

if CurrentState is WaitingForPickUp

LastState is WaitingForPickUp

Choose one of the following blocks of code based on ThisEvent

if ThisEvent is EF_Poke

RerequestAction()

subtract 1 from score

if ThisEvent is EF_EyesCovered

RerequestAction()

subtract 1 from score

if ThisEvent is EF_PickedUp

add 1 to score

if event param is 1

BuzzerOn is TRUE

BeepActive is TRUE

Start Beep timer for BEEP_TIME

TurnBuzzerOn()

CurrentState is WaitingForPutDown

else if event param is 2

BuzzerOn is TRUE

BeepActive is TRUE

Start Beep timer for BEEP_TIME

BeepCount is 2

TurnBuzzerOn()

CurrentState is WaitingForPutDown

else if event param is 3

BuzzerOn is TRUE

BeepActive is TRUE

Start Beep timer for BEEP_TIME

BeepCount is 3

TurnBuzzerOn()

CurrentState is WaitingForPutDown

if ThisEvent is EF_GameTimerExpired

See event notes at top of function

if ThisEvent is EF_ActionTimerExpired

See event notes at top of function

if ThisEvent is EF_Eyes_Timer_Expired

See event notes at top of function

if ThisEvent is EF_Ear_Timer_Expired

See event notes at top of function

if ThisEvent is EF_BeepTimerExpired

See event notes at top of function

if ThisEvent is EF_ActionSequenceTimerExpired

See event notes at top of function

end switch statement

if CurrentState is WaitingForPutDown

LastState is WaitingForPutDown

Choose one of the following blocks of code based on ThisEvent

if ThisEvent is EF_Poke

RerequestAction()

subtract 1 from score

if ThisEvent is EF_EyesCovered

RerequestAction()

subtract 1 from score

if ThisEvent is EF_PickedUp

if ThisEvent is EF_PickedUp

if event param is 1

BuzzerOn is TRUE

BeepActive is TRUE

Start Beep timer for BEEP_TIME

TurnBuzzerOn()

CurrentState is WaitingForPutDown

else if event param is 2

BuzzerOn is TRUE

BeepActive is TRUE

Start Beep timer for BEEP_TIME

BeepCount is 2

TurnBuzzerOn()

CurrentState is WaitingForPutDown

else if event param is 3

BuzzerOn is TRUE

BeepActive is TRUE

Start Beep timer for BEEP_TIME

BeepCount is 3

TurnBuzzerOn()

CurrentState is WaitingForPutDown

if ThisEvent is EF_PutDown

MakeHappyNoise()

TurnBuzzerOff()

CurrentState is WaitingBetweenActions

InterimActive is TRUE

Start Interim timer for INTERIM_TIME

Add 1 to score

if ThisEvent is EF_GameTimerExpired

See event notes at top of function

if ThisEvent is EF_ActionTimerExpired

See event notes at top of function

if ThisEvent is EF_Eyes_Timer_Expired

See event notes at top of function

if ThisEvent is EF_Ear_Timer_Expired

See event notes at top of function

if ThisEvent is EF_BeepTimerExpired

See event notes at top of function

if ThisEvent is EF_ActionSequenceTimerExpired

See event notes at top of function

end switch statement

if CurrentState is WaitingBetweenActions

Choose one of the following blocks of code based on ThisEvent

if ThisEvent is EF_GameTimerExpired

See event notes at top of function

if ThisEvent is EF_ActionTimerExpired

See event notes at top of function

if ThisEvent is EF_Eyes_Timer_Expired

See event notes at top of function

if ThisEvent is EF_Ear_Timer_Expired

See event notes at top of function

if ThisEvent is EF_BeepTimerExpired

See event notes at top of function

if ThisEvent is EF_ActionSequenceTimerExpired

See event notes at top of function

if ThisEvent is EF_InterimTimerExpired

InterimActiveFlag is FALSE

RandomlyPickNextState() such that NextState is not the same 					as LastState

RequestAction

ActionActiveFlag is TRUE

Start action active timer

CurrentState is NextState

end switch statement

end switch statement

end RunLazyLarrySM function

Motor Functions

/**************************************************************************** Motor Functions

Moves servo motors to assigned positions

Parameters: None

Returns: FALSE if error encountered, TRUE otherwise

Author Abigail Soong, 11/15/11

****************************************************************************/

boolean RightArmUp ()

if SERVO_RA to right arm up position does not encounter an error

return TRUE

else

return FALSE

boolean RightArmDown ()

if SERVO_RA to right arm down position does not encounter an error

return TRUE

else

return FALSE

boolean LeftArmUp ()

if SERVO_LA to left arm up position does not encounter an error

return TRUE

else

return FALSE

boolean LeftArmDown ()

if SERVO_LA to left arm down position does not encounter an error

return TRUE

else

return FALSE

boolean LowerArmsHalfWay (void)

if SERVO_RA to halfway position does not encounter an error

if SEVO_LA to halfway position does not encounter an error

return TRUE

else

return FALSE

boolean PutArmsDown (void)

if LeftArmDown() is not FALSE

if RightArmDown() is not FALSE

return TRUE

else

return FALSE

boolean PutArmsUp(void)

if LeftArmUp() is not FALSE

if RightArmUp() is not FALSE

return TRUE

else

return FALSE

boolean EarsWiggleOut()

if SERVO_RE to out position does not encounter an error

if SEVO_LE to out position does not encounter an error

EarsOut flag is TRUE

Start ear timer for EAR_TIME

return TRUE

else

return FALSE

boolean EarsWiggleIn()

if SERVO_RE to in position does not encounter an error

if SEVO_LE to in position does not encounter an error

EarsOut flag is FALSE

return TRUE

else

return FALSE

boolean OpenEyes()

if SERVO_EYES to open position does not encounter an error

return TRUE

else

return FALSE

boolean CloseEyes()

if SERVO_EYES to closed position does not encounter an error

return TRUE

else

return FALSE

EyesPosition() Function

/**************************************************************************** Function EyesPosition()

Increments eyes position between open and closed.

Parameters: None

Returns: boolean TRUE if an event was detected, FALSE otherwise

Author Katherine Spriggs, 11/20/11

****************************************************************************/

local variable travel is equal to the range of travel between open and closed

local variable position is equal to

eyes open value -(travel/45*CurrentEyesPosition)

if SERVO_EYES to position does not encounter an error

Add one to CurrentEyesPosition

return TRUE

else

return FALSE

end EyesPosition function

Noise Functions

/**************************************************************************** Noise Functions

Parameters: None

Returns: none

Author Katherine Spriggs, 11/20/11

****************************************************************************/

void TurnBuzzerOff(void)

Set port T4 hi

Start beep timer with BEEP_TIME

void TurnBuzzerOn(void)

Set port T4 lo

void Beep void

TurnBuzzerOn()

Set beep timer with BEEP_TIME

BuzzerOn flag is TRUE

BeepActive flag is TRUE

void MakeHappyNoise (void)

TurnBuzzerOn()

Set beep timer with BEEP_TIME

BeepActive flag is TRUE

BuzzerOn flag is TRUE

BeepCount is 1

RandomlyPickNextState() Function

/**************************************************************************** Randomly picks between WaitingForPoke, WaitingForEyesCovered, and WaitingForPickUp to assign the value of NextState

Parameters: None

Returns: none

Author Katherine Spriggs, 11/20/11

****************************************************************************/

local variable random is equal to some random number

if random <= (the max possible value of the random number)/3

NextState is WaitingForPickUp

else if random >= (the max possible value of the random number)(2/3)

NextState is WaitingForEyesCovered

else

NextState is WaitingForPoke

end RandomlyPickNextState function

RequestAction() Function

/**************************************************************************** Requests an action based on the variable NextState.  For example NextState is waiting for poke, wiggles ears to request poke.

Parameters: None

Returns: none

Author Katherine Spriggs, 11/28/11

****************************************************************************/

based on the value of NextState choose one of the following blocks of code

if NextState is WaitingForPoke

EarsWiggleOut()

if NextState is WaitingForEyesCovered

CloseEyes()  (This looks like a blink because eyes close and then 			return to incrementing position)

if NextState is WaitingForPickUp

PutArmsUp()

if NextState is waitingForPutDown

LowerArmsHalfWay()

end RequestAction function

RerequestAction() Function

/**************************************************************************** Rereequests an action based on the variable CurrentState. For example if CurrentState is waiting for poke and the user covers Larry’s eyes, this function will be called to rerequest the poke by wiggling Larry’s ears.

Parameters: None

Returns: none

Author Katherine Spriggs, 11/28/11

****************************************************************************/

based on the value of CurrentState choose one of the following blocks of code

if CurrentState is WaitingForPoke

EarsWiggleOut()

if CurrentState is WaitingForEyesCovered

CloseEyes()  (This looks like a blink because eyes close and then 		return to incrementing position)

if CurrentState is WaitingForPickUp

RerequestPickUp flag is TRUE

ActionSequenceActive flag is TRUE

if CurrentState is waitingForPutDown

RerequestPutDown flag is TRUE

ActionSequenceActive flag is TRUE

end RerequestAction function

Sequence Functions

/**************************************************************************** Sequence Functions including: HappyEndSequence, SadEndSequence, RerequestPickUp, RerequestPutDown

Parameters: None

Returns: none

Author Katherine Spriggs, 11/29/11

****************************************************************************/

void DoHappyEndSequence (void)

HappyEndSequence flag is TRUE

ActionSequenceActive flag is TRUE

void DoHappyEndSequenceAction (void

local static variable count is 0

if count is 0

PutArmsUp()

EarsWiggleOut

Set action sequence timer for ACTION_SEQUENCE_TIME

add 1 to count

else if count is 1

LeftArmDown()

Set action sequence timer for ACTION_SEQUENCE_TIME

add 1 to count

else if count is 2

RightArmDown()

LeftArmUp()

Set action sequence timer for ACTION_SEQUENCE_TIME

add 1 to count

else if count is 3

LeftArmDown()

RightArmUp()

Set action sequence timer for ACTION_SEQUENCE_TIME

add 1 to count

else if count is 4

RightArmDown()

LeftArmUp()

Set action sequence timer for ACTION_SEQUENCE_TIME

add 1 to count

else if count is 5

LeftArmDown()

ActionSequenceActive flag is FALSE

HappyEndSequence flag is FALSE

count is 0

void DoSadEndSequence (void)

SadEndSequence flag is TRUE

ActionSequenceActive flag is TRUE

void DoHappyEndSequenceAction (void

local static variable count is 0

if count is 0

PutArmsUp()

Set action sequence timer for ACTION_SEQUENCE_TIME

add 1 to count

else if count is 1

PutArmsDown()

ActionSequenceActive flag is FALSE

SadEndSequence flag is FALSE

count is 0

void DoRerequestPickUpAction (void)

local static variable count is 0

ActionSequenceActive flag is TRUE

if count is 0

PutArmsDown()

Set action sequence timer for ACTION_SEQUENCE_TIME

add 1 to count

else if count is 1

PutArmsUp()

ActionSequenceActive flag is FALSE

RequestPickUp flag is FALSE

count is 0

void DoRerequestPutDownAction (void)

local static variable count is 0

ActionSequenceActive flag is TRUE

if count is 0

PutArmsUp()

Set action sequence timer for ACTION_SEQUENCE_TIME

add 1 to count

else if count is 1

LowerArmsHalfWay()

ActionSequenceActive flag is FALSE

RequestPickUp flag is FALSE

count is 0

Check-flag Functions

/**************************************************************************** Check-flag Functions including: IsGameActive, IsActionActive, IsPickedUp, IsBeepActive, EarsAreOut, IsInterimActive, IsEyesClosed, IsActionSequenceActive

Parameters: None

Returns: none

Author Katherine Spriggs, 11/29/11

****************************************************************************/

boolean IsGameActive (void)

return GameActiveFlag

boolean IsActionActive (void)

return ActionActiveFlag

boolean IsBeepActive

return BeepActive flag

boolean EarsAreOut

return EarsOut flag

boolean IsInterimActive

return InterimActive flag

boolean IsActionSequenceActive (void

return ActionSequenceActiveFlag